## Slide 1
Samantha.Molnar@colorado.edu
The Role of Inertia in the Cascading-Failure Dynamics of Power Systems
Samantha Molnar1,2, Elizabeth Bradley1, Bri-Mathias Hodge2, Kenny Gruchalla2
1 Department of Computer Science, University of Colorado, Boulder, CO, USA
2 National Renewable Energy Lab (NREL), Golden, CO, USA
Topology | ▶︎ | Delauney Triangulation and minimum spanning tree
Load | ▶︎ | Population size Power Consumption
Generation | ▶︎ | Amount and type from EIA
Line Parameters | ▶︎ | Statistically pick radius and conductor type
Dynamical Parameters | ▶︎ | Draw from distributions of known cases
Topology | ▶︎ | Delauney Triangulation and minimum spanning tree
Load | ▶︎ | 
Generation | ▶︎ | Amount and type from EIA
Line Parameters | ▶︎ | Statistically pick radius and conductor type
Dynamical Parameters | ▶︎ | Draw from distributions of known cases
Generation Type | (MW・s)
Nuclear | 5344-6530
Coal | 863-3158
Solar | 0
Generation Type | 
Nuclear | 5344-6530
Coal | 863-3158
Solar | 0
In general, contingencies that are closer to large-inertia generation cause a higher frequency deviation. However, there are some exceptions: denoted by a blue point. This indicates a more complicated relationship with network topology.
Test Cases
Problem:
  U.S power grids are considered critical infrastructure → Data is not public
Solution:
  Create synthetic networks that statistically match real power grid characteristics
Cascading Failures
Model
September 21, 2016: A fire at Aguirre Power Station in Puerto Rico causes a cascading failure resulting in an island-wide blackout. Image from [1].
Overview
Power systems today are undergoing extreme changes with the integration of renewable generation sources such as solar and wind. Traditional generation sources, such as coal and natural gas, provide inertial support, which helps maintain system stability when an outage occurs. However, solar and wind generation do not, on their own, provide this support, which potentially makes the system more vulnerable to failures
As total system inertia decreases, the maximum frequency deviation and the RoCoF increase. Furthermore, the trend is non-linear.
We compute the system frequency for each cascading failure simulation to quantify the resulting dynamics. Frequency stability is a growing concern as more renewable generation is added to power systems.
Frequency Stability
References
NASA Earth Observatory. Puerto Rico Goes Dark. https://earthobservatory.nasa.gov/images/88796/puerto-rico-goes-dark . Accessed: 3-2-2019.
How does total system inertia impact power system stability during cascading failures?
Average Inertia Distance
Total System Inertia
Inertia
We use the average inertia distance to understand how topology plays a role in frequency stability. Although the
Illinois
South Carolina
The inertia constant of a generator indicates how much energy it can stores in its rotation. It is a combination of the turbine size and maximum power of the generator
Conclusions
As total system inertia decreases power system frequency dynamics will increase non-linearly. Furthermore, these dynamics are dependent on the structure of the network, illustrated by the dependence of the maximum frequency deviation on the average inertia distance. However, the structural dependence is not entirely captured by the average inertia distance which suggests that